## Slide 1
Deryck James and Melvin Felton
Atmospheric Sensing Branch
Computational and Information Sciences Directorate
24 06 2019
Introduction to Remote Sensing and Army Research Laboratory use of Doppler Lidar Technology
Approved for public release

## Slide 2: Introduction: Why the Army researches the environment
Challenges posed to the Army by the battlefield environment
-There are weather hazards posed to: soldiers, autonomous agents (robots), manned and unmanned
vehicles (ground, air, and sea), accurate delivery of Army payloads (airdrop), etc.
-The environment also impacts: the transmission of signals for communication, the transmission of acoustic
signals generated by vehicular and munitions activity on the battlefield, transport and dispersion of
aerosols/pollution/chem-bio weapons on the battlefield, etc.
-Therefore, Army scientists research the
environment to ensure increased forecast
accuracy, resulting in significant efficiencies
and cost savings for Army operations.

## Slide 3: Measurement
-We measure the environment using a variety of different
experimental techniques to acquire information about it.
-In order to acquire information about the environment, there
must be some form of interaction between an instrument and
the environment.
-There are two types of interaction: local and remote.

## Slide 4: Examples of local measurements
-Airmar Weather Station: wind speed and direction, air temperature, pressure, relative humidity
-Radiosonde: an instrument carried into the
atmosphere by a balloon that measures various
atmospheric parameters and transmits them by radio
to a ground receiver. Radiosondes provide
measurements of altitude, pressure, temperature,
relative humidity, wind (both wind speed and wind
direction), etc.

## Slide 5: Remote Sensing
-Without direct physical contact between the instrument and the
environment, some remote interaction must be introduced to carry
away the environmental information.
-The interaction between radiation and the environment is the
most common interaction used in modern remote sensing.
-The radiation includes electromagnetic radiation and acoustic
waves.
-Remote sensing can be either passive or active.

## Slide 6: Remote sensing—passive
-Passive Remote Sensing: no self-generated radiation is used in
the sensing; uses naturally occurring radiation, such as sunlight or
thermal emission instead; passive systems are instruments that
receive information naturally emitted from an object or a region in
the atmosphere.
-Examples include: conventional photography, thermal imagers,
spectrometers, interferometer, etc.

## Slide 7: Remote sensing—passive (cont’d)
Visible and Thermal Imagers
Directional Microphone

## Slide 8: Remote sensing—active
-Active Remote Sensing: self-generated radiation sources are
used, such as laser light, radio- and micro-waves, acoustic wave:
LIDAR: Light Detection And Ranging
RADAR: Radiowave Detection And Ranging
SODAR: Sound Detection And Ranging
-All three of these technologies are based on the same principle:
radiation is transmitted from the instrument into environment,
backscattered by objects in the environment, and then detected
and analyzed by receivers on the instrument.

## Slide 9: Remote sensing—active (cont’d)
Radar
Lidar

## Slide 10: Remote sensing—applications
-Applications in academia, government, and industry:
Atmospheric Research
Environmental Research
Solid-Earth Research
Ocean Research
Space Exploration
Astronomy Exploration
Airport Safety
Wind turbine and wind farm
and many more ...

## Slide 11: Remote sensing—advantages
-Advantages of Remote Sensing:
Reaching inaccessible/difficult regions to make reliable measurements
Avoiding hazardous regions
Fast and inexpensive probing of large volumes
Minimal disturbance of measured processes
-Advantages of Active Remote Sensing:
Independence of natural radiation sources;
Reduced sensitivity to background light (time of day);
High intensity of stimulating signal;
Control of stimulating signal;
Capable of line profiles, 2D coverage, and 3D coverage– all as a function of time

## Slide 12: Doppler lidar—how we use them
Urban transport and dispersion: Pentagon Shield

## Slide 13: Doppler lidar—how we use them (cont’d)
Wind flow in complex mountain terrain:
MATERHORN (Mountain Terrain Atmospheric Modelling and Observations)

## Slide 14: Doppler lidar—how we use them (cont’d)
Coastal wind flow:
CASPER (coupled air-sea processes and electromagnetic ducting research)

## Slide 15: Doppler lidar—how we use them (cont’d)
Wake vortex detection

## Slide 16: Doppler lidar—how we use them (cont’d)
Paratrooper support

## Slide 17: Doppler lidar—how we use them (cont’d)
Hampton University collaboration:
Combine multiple lidar types to study the lower atmosphere

## Slide 18: Doppler lidar—how we use them (cont’d)
Wind flow during urban heat wave:
LISTOS (Long Island Sound Tropospheric Ozone Study)

## Slide 19: Wakimoto et Al. (BAMS,1996)

## Slide 20: Wakimoto et Al. (BAMS,1996) cont’d

## Slide 21: Wakimoto et Al. (BAMS,1996) cont’d

## Slide 22: Wakimoto et Al. (BAMS,1996) cont’d